## Serial protocol to send building information to Arduino

Byte #	Type	Description	Value or Example
0	uint8_t	First byte of the envlope start	0xA5
1	uint8_t	Second byte of the envlope start	0x5A
2	uint8_t	Number of building packets	0-255
3	uint8_t	~Number of buildings	0-255
4	BuildingStatusRecord_t	Status of building N	See below (current length is 28 bytes)
Last	uint8_t	CRC	XOR of all bytes starting with byte 2. / Initial value 0x10101010

typedef struct {
  uint32_t        id;
  UtilityStatusRecord_t grid;
  UtilityStatusRecord_t solar;
  UtilityStatusRecord_t battery;
  UtilityStatusRecord_t generator;
} BuildingStatusRecord_t;

typedef struct {
  uint8_t   id;
  uint8_t   status;   //  combination of UtilityStatus_t 's
  uint8_t   capacity; //  0-100%
  uint16_t  output;   //  kWh
} UtilityStatusRecord_t;

Total payload for 16 buildings is 453 bytes.

Both esp32 and Arduino are little-endian

## Serial Comms btw esp32 and Arduino:
1. Using level shifter

2. Using voltage divider